## Slide 1
Project Visibility and Contrast
“I think having land and not ruining it is the most beautiful art anybody could want to own.” - Andy Warhol

## Slide 2
What makes projects visible?
What are the visual characteristics of large-scale projects, especially energy projects?
  Wind Energy
  Solar Energy
  Electric Transmission
How far can you see them?
What distances matter?
Project Visibility and Contrast
Topics

## Slide 3
Many variables – called “visibility factors” – affect the visibility of an object in the landscape.
Project Visibility and Contrast
What Makes Projects Visible?
And they all interact…

## Slide 4
Viewer Characteristics
  Visual Acuity
  Viewer Engagement and Experience
  Viewer Motion
Project Visibility and Contrast
What Makes Projects Visible?

## Slide 5
Viewshed Limiting Factors
  Topographic Screening
  Vegetative Screening
  Structural Screening
  Viewer Height
  Target Height
  Earth Curvature
  Atmospheric Refraction
Project Visibility and Contrast
What Makes Projects Visible?

## Slide 6
Lighting
  Solar Altitude and Azimuth
Project Visibility and Contrast
What Makes Projects Visible?

## Slide 7
Lighting
  Weather and Climate
Project Visibility and Contrast
What Makes Projects Visible?

## Slide 8
Distance
Project Visibility and Contrast
What Makes Projects Visible?

## Slide 9
Viewing Geometry
  Viewer Position
Project Visibility and Contrast
What Makes Projects Visible?

## Slide 10
Viewing Geometry
  Aspect
Project Visibility and Contrast
What Makes Projects Visible?

## Slide 11
Object Visual Characteristics
  Size
  Form and Line
  Color and Texture
  Motion
Project Visibility and Contrast
What Makes Projects Visible?

## Slide 12
Backdrop
Project Visibility and Contrast
What Makes Projects Visible?

## Slide 13
Very Large Facilities
  Approved or under construction:
  Onshore wind facility of 1,000 turbines on more than 200,000 acres in Wyoming (312 mi2); Boise = 80 mi2
  Offshore wind facility up to 50,000 acres in Sweden (78 mi2)
  Solar facility up to 8,000 acres in California (12.5 mi2)
  Transmission lines hundreds of miles long
Project Visibility and Contrast
Renewable Energy Facilities
Desert Sunlight Solar Facility - 6.2 mi2
Boise from Space

## Slide 14
Very Tall Structures
  Offshore wind turbines more than 700 ft tall (Vestas V164-8MW)
  Onshore wind turbines more than 650 ft tall (Enercon E-126/7.5 MW)
  Current solar power tower 640 ft (Crescent Dunes)
Project Visibility and Contrast
What Makes Projects Visible?
Zion’s Bank Building - 323 ft.

## Slide 15
Highly Reflective Surfaces
  Wind turbines are white (per FAA requirements).
  Solar facilities can cause painfully bright glare at 20 mi.
  Transmission lines and insulators can cause glare.
Project Visibility and Contrast
Renewable Energy Facilities

## Slide 16
Rectilinear, Ordered Geometry
  Many regular polygons
  Highly structured and regular spatial arrangement
  Perfectly smooth or ordered surface textures
  Some introduce strong line contrasts
  Don’t blend well with “organic” landscapes
Project Visibility and Contrast
Renewable Energy Facilities

## Slide 17
Long Distance Visibility
  Wind turbines visible beyond 35 miles in western landscapes, strong contrasts beyond 13 mi.
  Offshore wind turbines visible beyond 25 mi, strong contrasts beyond 10 mi.
  Solar power towers easily visible at 35 mi, strong contrasts beyond 20 mi.
  Visible at same distances at night.
  Transmission visible beyond 15 mi, strong contrasts to a few miles.
Project Visibility and Contrast
How Far Can You See Them?

## Slide 18
Windfarm Visibility Analysis
Project Visibility and Contrast
What Distances Matter?
For 3 wind farms in Wyoming and Colorado
Average Visibility Rating (AVR)
1-2 = low contrast
3-4 = moderate contrast
5-6 = high contrast, dominates view
Wind facilities often dominated views beyond 10 mi
Easily visible beyond 20 mi
Under optimal conditions, visible beyond 35 mi
Synchronized flashing red lights visible beyond 35 mi at night

## Slide 19
Transmission Visibility Analysis
Project Visibility and Contrast
What Distances Matter?
For three 500 kV lattice tower facilities in Idaho, Nevada, and California
Average Visibility Rating (AVR)
1-2 = low contrast
3-4 = moderate contrast
5-6 = high contrast, dominates view
Facilities sometimes dominated views beyond 2 mi.
Sometimes easily visible beyond 5 mi
Under optimal conditions, visible beyond 15 mi
Very sensitive to backdrop

## Slide 20
Solar Visibility Analysis
  No formal study, but:
  Small parabolic trough facility (300 acres) easily visible at 14 mi
  Small photovoltaic facility visible beyond 20 mi
    Both not recognizable as solar facilities at long distances
  Ivanpah Power Tower facility easily visible at 35 mi, likely visible at much greater distance
Project Visibility and Contrast
What Distances Matter?
Ivanpah Solar Power Tower Facility at 35 mi
Parabolic trough and photovoltaic facilities at 10 mi

## Slide 21
Highly Visible at Night
  Synchronized flashing lights on wind turbines
  Power block lighting at solar facilities
  Transmission substations
  Generally visible as far or farther than during the day
Project Visibility and Contrast
What Distances Matter?
Nevada Solar One facility (left) and substation (right), Nevada
Cedar Creek Windfarm, Colorado

## Slide 22
Conclusion
Project Visibility and Contrast
What Distances Matter?
Large facilities + large structures + highly reflective surfaces + rectilinear geometry + moving parts + glare + lighting + sited in open landscapes = long-distance visibility.
Ivanpah Solar Power Tower Facility, California

## Slide 23
For More Info
Project Visibility and Contrast
What Distances Matter?
sullivan@anl.gov