## Slide 2
Contrast Rating

## Slide 3
Determine the elements of a project that are inconsistent with VRM objectives and recommend measures to improve the visual quality of the project
The VRM System is about minimizing visual contrast.
The Contrast Rating process
First, determines whether a proposal conforms to the current Land Use Plan, and
Second, supports the subsequent impact analysis process
Contrast Rating
Unit Objective

## Slide 4
A systematic process used to analyze potential visual impacts of proposed projects and activities
  BLM Handbook 8431-1
The amount of contrast is measured by separating the landscape into major features
  Landform/water, vegetation, and structures
  Use “language of landscapes” when describing
Then predicting the magnitude of contrast in each of the basic elements
  Form, line, color, and texture
Contrast Rating
Process

## Slide 5
Quickly reveals elements and features that cause the greatest visual impact
Intended to assist BLM personnel not formally trained in the design arts to apply basic principles of planning and design to prevent or minimize visual impacts
Every attempt should be made to reduce visual impacts even if a project meets VRM objectives for the area
Contrast Rating
Process

## Slide 6
The contrast rating should be completed in the field from the selected KOP(s) and should be completed by an interdisciplinary team
Do not fill out forms as a “desk exercise,” it is important to get out on the ground to see the context of the proposed project and its location
The contrast rating should be completed during the time of year and time of day when most people will be viewing the area of development
Contrast Rating
Tips

## Slide 7
Work with project proponent early in the project planning process, this will help prevent surprises later!
  1 – Obtain a complete project description
  2 – Identify VRM objectives from land use plan
  3 – Select Key Observation Points (KOPs)
  4 – Prepare visual simulations (optional)
  5 – Complete contrast rating
Contrast Rating
Steps

## Slide 8
Obtain a complete project description
  Emphasize early contact with project proponent
  Coach proponent on project design
  Project proposal must be comprehensive
Contrast Rating
Step 1

## Slide 9
Identify VRM objectives from the land use plan
  Familiarize yourself with your land use plan
  Identify VRM objective
    What is the existing management class for the project location, and why?
  Involve interdisciplinary team
  Understand other resource issues
Contrast Rating
Step 2

## Slide 10
Class I
  Preserve the existing character of the landscape
  Manage for natural ecological changes
  Change allowed: very low
  Activities should not be visible and must not attract attention
Class II
  Retain the existing character of the landscape
  Change allowed: low
  Activities may be visible, but should not attract attention
Contrast Rating
VRM Class Objectives

## Slide 11
Class III
  Partially retain the existing character of the landscape
  Change allowed: moderate
  Activities may attract attention but should not dominate the view
Class IV
  Provide for management activities which require major modification of the existing character of the landscape
  Change allowed: high
  Activities may attract attention, may dominate the view, but are still mitigated
Contrast Rating
VRM Class Objectives

## Slide 12
Select Key Observation Points (KOPs)
  What is a KOP?
    A critical viewpoint or place from
    which we analyze the visual impact
    of a proposed project
Types of KOPs
  KOPs should be places from which a proposed project is seen by large numbers of viewers or critical viewers
  Where view of proposed project is most revealing
  Single Points – trailheads, campgrounds, scenic overlooks, parking lots, subdivisions, and towns
  Linear – roads, trails, and rivers
Contrast Rating
Step 3

## Slide 13
Factors in KOP selection
  (Remember the Environmental Factors!)
    Angle of observation
    Number of viewers
    Length of time the project is in view
    Relative project size
    Season of use
    Light Conditions
How many KOPs are needed?
  Linear projects should have more than one
  Dependent on the size of the project, land use plan direction, locations from where it can be seen
Contrast Rating
Step 3

## Slide 14
When are KOPs selected?
  Early in the project planning
  process
Who selects them?
  Interdisciplinary team
  Input from proponent
  Coordination with other agencies
    Examples - NPS and USFS
Accuracy is important!
  Location can sway results
Contrast Rating
Step 3

## Slide 15
Prepare visual simulations (optional)
  Complex projects may benefit from visual simulations
  Provides visual representation of a project before and after
    Highlights impacts and potential mitigation measures
    Good way to illustrate impacts in NEPA analysis
    Seeing an image of a project is much more powerful than trying to imagine it
    Helps eliminate bias
    Allows all team members to see the project the same
    Helps the proponent, public, and the BLM
Contrast Rating
Step 4

## Slide 16
Contrast Rating
Step 4 – Visual Simulations Example
Before – Existing Conditions
“After” Simulation
Mitigated Simulation

## Slide 17
Complete Contrast Rating
  Visual Contrast Rating Worksheet – BLM Form 8400-4
  See BLM Handbook H-8431-1
  Validates Land Use Plan Conformance
  Provides documentation for NEPA
  Provides a record for future action
  Helps defend against appeals
Contrast Rating
Step 5
Notes: Validates plan conformance … or pinpoints where to focus design alterations to meet plan objectives and further minimize impacts.

## Slide 18
Contrast Rating
Worksheet

## Slide 19
Contrast Rating
Worksheet
Section A
  Locates the project and identifies the VRM class
  A simple illustration or map identifies the project location and KOP

## Slide 20
Contrast Rating
Worksheet
Section B
  Where the existing characteristic landscape of the project area is described (use “language of landscapes”)
  Focus on the area being affected by the project

## Slide 21
Contrast Rating
Worksheet
Section C
  Where the proposed activity’s effects on the characteristic landscape are described

## Slide 22
Contrast Rating
Worksheet
Section D
  Organized into features (land/water, vegetation, and structures) and elements (form, line, color, and texture)
  The terms strong, moderate, weak, and none conform to VRM Classes IV, III, II, and I, respectively
    For example – if the project creates strong contrast (impacts), it would conform to the class IV objective but not to the class I – III objectives
    If a project only causes weak contrast (impacts), it would meet the Class II VRM objective

## Slide 23
Contrast Rating
Worksheet
Section D
  In this example, the project would meet the VRM Class III objective for form, but only a VRM Class IV objective for line, color, and texture

## Slide 24
Contrast Rating
Worksheet
Section D
  This tells you where to focus mitigation efforts in order to reduce the degree of impact, and thus meet the VRM objective

## Slide 25
Contrast Rating
Worksheet – Degree of Contrast Criteria
None
  Contrast not visible or perceived
  Corresponds to VRM Class I
Weak
  Contrast seen but does not attract attention
  Corresponds to Class II
Moderate
  Contrast attracts attention but does not dominate view
  Corresponds to Class III
Strong
  Contrast demands attention and is dominant
  Corresponds to Class IV

## Slide 26
Contrast Rating
Worksheet
Section D (Continued)
  Where you can provide further explanation of why a project does or does not meet VRM objectives
  As in this example, changes to Land and Vegetation would cause a moderate degree of contrast to the element line, with strong contrast from Structures
  The element line is a focus of mitigation efforts for this project

## Slide 27
Contrast Rating
Worksheet
Section D (Continued)
  Where you can provide recommended mitigation measures
Proposed
Mitigated

## Slide 28
Contrast Rating
Process (Continued)
Document! Document! Document!
  Take pictures
  Complete the form
  Write short narratives
  Prepare visual simulations (optional)
  Do whatever you need to do to describe your thought process and final recommendations
  Documentation is the only way you or your manager will accurately remember what took place during your analysis
  And if challenged, no documentation = didn’t happen

## Slide 29
  Does project meet VRM Objectives?
  YES, if: None = Class I
  Weak = Class II
  Moderate = Class III
  Strong = Class IV
Contrast Rating
Conformance with VRM Objectives

## Slide 30
  Does project meet VRM Objectives?
  NO, what to do?
  Redesign project to meet VRM Objectives
  Internally initiated – Drop project
  Externally initiated – Deny application for project
  Amend RMP only as a last resort
    Address reasons for the current VRM Class designation
    Assess Compensatory Mitigation
Contrast Rating
Conformance with VRM Objectives

## Slide 31
Contrast Rating
Process (Continued)
Input information into NEPA document
  Enter your findings, along with necessary documentation
  Write any necessary stipulations
    Be sure all resource stipulations are coordinated and in agreement
Continue to work with the project proponent through all phases of the project (pre-construction, construction, and reclamation) to ensure project is completed as planned and stipulations are being followed!
Patience! It may take years before you see the outcome of all your efforts

## Slide 32
Contrast Rating
Example – Habitat Enhancement
1 – Obtain a complete project description
  Habitat enhancement project for bighorn sheep
  Site was selected for its potential to allow sheep to access suitable habitat
  Habitat treatment would include a combination of clear cutting, heavy thinning, and group thinning
  Treatment area would be approximately 300 yards wide and would encompass approximately 200 acres
  Project design features will be used to minimize the visual impact of the project, including clumping and feathering of the treatment edges to prevent distinct lines, and pruning the lower limbs of the leave trees to maintain portions of intact canopy while still providing sightlines for sheep

## Slide 33
Contrast Rating
Example – Habitat Enhancement
2 – Identify VRM objectives
from land use plan
  Class II
    Retain landscape character
    Change allowed: low
    Visible but should not attract
    attention
  Class III
    Partially retain landscape
    character
    Change allowed: moderate
    Can attract attention but
    should not dominate view

## Slide 34
Contrast Rating
Example – Habitat Enhancement
3 – Select Key Observation
Points (KOPs)
  Linear feature – State
  Highway 50
  6 KOPs were selected based
  on viewshed analysis and
  from environmental factors
  (e.g. angle of view, season
  of use, duration in view)

## Slide 35
Contrast Rating
Example – Habitat Enhancement
4 – Prepare visual simulations (optional)
  KOP 1
Before – Existing Conditions
After Simulation

## Slide 36
Contrast Rating
Example – Habitat Enhancement
5 – Complete contrast rating

## Slide 37
Contrast Rating
Example – Habitat Enhancement
5 – Complete contrast rating

## Slide 38
Contrast Rating
Example – Habitat Enhancement
5 – Complete contrast rating

## Slide 39
Contrast Rating
Example – New Natural Gas Well Pad
1 – Obtain a complete project description
  Proposal to drill 8 new federal wells from a new well pad with new access road on land administered by the BLM
  Well pad would have a maximum cut slope of 33.1 feet at the southwest corner and a maximum fill slope of 25.2 feet at the northwestern corner
  The road would be approximate 0.4 mile in length and 20-feet in width
  The road grade would vary from 5% to 10%
  Installation of a temporary pipeline
  Construction would involve approximately 7.9 acres of new surface disturbance, which would be reduced to approximately 2.5 acres after interim reclamation

## Slide 40
Contrast Rating
Example – New Natural Gas Well Pad
2 – Identify VRM objectives
from land use plan
  Class II
    Retain landscape character
    Change allowed: low
    Visible but should not attract
    attention
  Class III
    Partially retain landscape
    character
    Change allowed: moderate
    Can attract attention but
    should not dominate view

## Slide 41
Contrast Rating
Example – New Natural Gas Well Pad
2 – Identify VRM objectives
from land use plan
  Class IV
    Provide for management
    activities which require
    major modification to the
    character of the landscape
    Change allowed: high
    Activities may attract
    attention, may dominate the
    view, but is still mitigated

## Slide 42
Contrast Rating
Example – New Natural Gas Well Pad
3 – Select Key Observation
Points (KOPs)
  Linear features – State
  Highway 6 and County Road
  300
  3 KOPs were selected based
  on field analysis and
  from environmental factors
  (e.g. angle of view, season
  of use, duration in view)

## Slide 43
Contrast Rating
Example – New Natural Gas Well Pad
4 – Prepare visual simulations (optional)
  KOP 2
Before
After
During Construction
Before – Existing Conditions
Simulation - Mitigated
Notes: “Interim” mitigation v longer-term restoration (later)

## Slide 44
Contrast Rating
Example – New Natural Gas Well Pad
5 – Complete contrast rating

## Slide 45
Contrast Rating
Example – New Natural Gas Well Pad
Patience........................
During Construction
Post mitigation
Notes: It can take years to see the outcome of all the effort, particularly relating to reclamation that meets BLM standards.

## Slide 46
Contrast Rating
Classroom Exercise – Red Rock View Mine
Notes: Visual Contrast Rating Assignment: Red Rock View Mine
Project Background
After recently attending VRM training, your group has been asked to conduct a contrast rating for a mining operation proposed along the southeast side of Red Rock Canyon National Conservation Area by Red Rock Estates Minery & Casino, LLC. Controversy over this project is escalating as local communities raise concern with the amount of mining that has continued adjacent to the National Conservation Area. There are also concerns about this project being in direct view of a segment of the Old Spanish Trail. Additionally, a national scenery advocacy group, in response to a proposed luxury residential development just to the north near the Red Rock Canyon Visitor Center, has just announced on their website that the Red Rock Canyon State Scenic Byway (State Route 159) has one of the ten most endangered vistas in the country.
Project Overview
The first phase of the mining operation would develop a 15-acre open pit mine. This would be in operation for an anticipated duration of approximately 2 years. The second phase would expand the open pit mine to 40 acres (as shown in the visual simulation). The life-cycle of the mine is anticipated to run for approximately 10 years.
In addition to the open pit mine, there would be an administrative structure built, measuring approximately 150’ x 100’. There would also be frequent truck traffic entering the mine from SR 159. Heavy equipment would also be actively used in conjunction with routine mine operations. It is anticipated that operations would occur 16 hours per day to maximize productivity of the mine. Lighting would be used during dark hours.
At the end of the 10-year operation period, the mine would be decommissioned. Erosion control measures would be taken to ensure no offsite contamination occurs. Minimal recontouring and revegetation would be done.
VRM Information
The Red Rock Canyon NCA RMP designates this area, on the opposite side of SR 159 from the Red Rock escarpment, as VRM III due to its proximity to the NCA.
Assignment
Your field manager asked your group to determine whether the project, as proposed, would meet the VRM Class III objectives and, if not, what mitigation measures might bring it into conformance with VRM Class III objectives.