## Slide 3
Provide a Foundation
  Initiate and/or conduct an inventory
  Provide oversight to a contracted inventory
Unit Objective

## Slide 4
Systematic Process
  Determine extent and quality of visual resources
    BLM Handbook 8401-1
Quantitative
  Objective
  Repeatable
Outcome
  Baseline data
    Land use planning process (fulfilling FLMPA)
    Affected environment (fulfilling NEPA)
Philosophy & Process

## Slide 5
Inventory leads to VRI classes
VRI = Snapshot of existing condition
Management decisions leads to VRM classes
VRM = level of allowable change to visual resources
Practical value

## Slide 6
Philosophy & Process
Distance Zones
Visual Resource Inventory
Scenic Quality Evaluation
Sensitivity Level Analysis
VRI Classification

## Slide 7
Inventory Factors
Inventory Factor | Rating & meaning
Scenic Quality Rating What does it look like? | Measure of the visual appeal of a tract of land A (most variety and quality) B C (least variety and quality)
Sensitivity Level Rating Importance to the Public? | Measure of willingness to accept visual change to the existing landscape Low (most willing) Moderate High (least willing )
Distance Zone Where do people view the landscape and how? | Measure of visibility from travel routes or observation points Foreground/Middleground (0-5 miles) Background (5-15 miles) Seldom Seen (15+ miles or shielded from view)

## Slide 8
The VRI class is different than the VRM class
  VRI Class 1: NOT BASED ON INVENTORY – Assigned to areas where a decision has been made previously to maintain a natural landscape. These areas reflect a management decision, not based on inventory. (e.g. Wilderness Areas)
  VRI Class 2: High overall visual value based on inventory
  VRI Class 3: Moderate overall visual value based on inventory
  VRI Class 4: Low overall visual value based on inventory
The VRI class offers a quick understanding of an area’s overall visual value yet does not replace the need to understand the 3 underlying factors and their ratings
VRI Class Definitions

## Slide 9
How are VRI classes determined?
VRI Class Determination Table

## Slide 10
Geodatabase
  A collection of geographic datasets
    polygons, polylines, and point spatial data
  Format used for editing and data management
  A series of tables holding information linked to the spatial data
VRI Geodatabase
  Supplementary to the Visual Resource Inventory Handbook
    H-8410-1
  For more information:
    https://www.blm.gov/policy/im-2012-055
VRI National Data Standard

## Slide 11
Scenic Quality Analysis

## Slide 12
Scenery is defined as…
  “a view of natural features (such as mountains, hills, valleys, etc.) that is pleasing to look at; the things that can be seen where a person lives, works, etc.”
Quality is defined as…
  “peculiar and essential character”
Scenic quality is a description of the landscape features and characteristics that work to define one area as different than another
What is Scenic Quality?

## Slide 13
A measure of the visual appeal of a tract of land
  All lands have scenic value
    Areas with the most variety and the most harmonious composition have the greatest scenic value
Evaluation of scenic quality is done in relationship to the natural landscape on a comparative basis with similar features within the same physiographic province
Lands are given an A, B, or C rating based on the apparent scenic quality which is determined by 7 key factors
Scenic Quality Criteria

## Slide 14
Conducted by an interdisciplinary team
Evaluated by observing the area from several locations
Each location becomes an inventory observation point
(IOP) and a photographic record is maintained
Each unit is scored and recorded on the BLM Scenic Quality Rating Form 8400-1
Scores reflect the overall impression of the area
General Guidelines

## Slide 15
1) Delineate Scenic Quality Rating Units (SQRU)
4) Create Photo Record
3) Make Field Observation Record
5) Evaluate, Score, and Categorize
2) Choose Inventory Observation Points
6) Enter Data into VRI Geodatabase
Visual Resource Inventory
Sensitivity Level Analysis
Public Land Visibility
Scenic Values Held by People expressed as a concern/attitude toward visual change
Delineation of Distance Zones
Land Features & Characteristics
Scenic Quality Evaluation
Scenic Quality Evaluation Process

## Slide 16
The planning area is subdivided into scenic quality rating units for rating purposes and are delineated on a basis of:
  Similar physiographic characteristics
  Similar visual patterns – texture, color, variety etc.
  Areas that have similar impacts from man-made modifications
Different methods for delineating units include:
  Drawing units onto paper topo maps and/or aerial photos
  Digitizing directly into GIS
The size of units may vary depending on the homogeneity of the landscape or detail desired and can be fine-tuned in the field by ground-truthing
Step 1 – SQRU Delineation

## Slide 17
Visual Resource Inventory
Step 1 – SQRU Delineation

## Slide 18
Visual Resource Inventory
Step 1 – SQRU Delineation
Boise
Notes: Ecoregions denote areas of general similarity in ecosystems and in the type, quality, and quantity of environmental resources; they are designed to serve as a spatial framework for the research, assessment, management, and monitoring of ecosystems and ecosystem components. By recognizing the spatial differences in the capacities and potentials of ecosystems, ecoregions stratify the environment by its probable response to disturbance (Bryce and others, 1999). These general purpose regions are critical for structuring and implementing ecosystem management strategies across federal agencies, state agencies, and nongovernment organizations that are responsible for different types of resources within the same geographical areas (Omernik and others, 2000).

## Slide 19
Tools
Step 1 – SQRU Delineation

## Slide 20
How many SQRU do you see in this image?
Step 1 – SQRU Delineation

## Slide 21
How many SQRU do you see in this image?
Step 1 – SQRU Delineation

## Slide 22
How many SQRU do you see in this image?
Step 1 – SQRU Delineation

## Slide 23
Step 1 – SQRU Delineation

## Slide 24
Step 1 – SQRU Delineation

## Slide 25
Step 1 – SQRU Delineation
Boise

## Slide 26
Inventory Observation
Points (IOPs) are used to
  Evaluate each SQRU
  from several viewpoints
    (H 8410-1, II(B))
Examples
  Logical stopping places
    Overlooks
    Trailheads
    Campgrounds etc.
  Travel corridors
    Trails, rivers, roads
Visual Resource Inventory
Step 2 – Select IOPs
Boise

## Slide 27
Select IOPs based on the visual vantage
  Find locations from where you can assess the overall
  landscape character of the unit
Examples of where to observe each SQRU
  From one or more stopping places inside the SQRU
  While driving through the SQRU
  From a distant vantage point outside of the SQRU
IOPs are not the same as a KOPs!
Step 2 – Select IOPs

## Slide 28
Visual Resource Inventory
Step 1 – SQRU Delineation

## Slide 29
Visual Resource Inventory
Step 3 – Field Observation Record
Colorado Plateau
Southern Rockies
Notes: Comparing apples to apples versus apples to oranges. Do I want to have apples and oranges as props?

## Slide 30
Visual Resource Inventory
Step 3 – Field Observation Record
Colorado Plateau
Colorado Plateau

## Slide 31
Field Inventory
  Write descriptions using
  “language of landscapes”
    2. Landscape character
    elements
      Form
      Line
      Color
      Texture
    3. Landscape type &
    analysis factors
Step 3 – Field Observation Record

## Slide 32
Score Determined using
7 key factors
  Landform
  Vegetation
  Water
  Color
  Adjacent Scenery
  Scarcity
  Cultural Modifications
Step 3 – Field Observation Record

## Slide 33
Field Inventory
  Scoring the 7
  Key Factors
Based on the score,
SQRUs are given a
Rating of A, B, or C
Note: Reassess and
adjust if final score
falls between
threshold of A & B
(18.5) or B & G (11.5)
Visual Resource Inventory
Step 3 – Field Observation Record

## Slide 34
Landform
  Topography gets more interesting as it gets steeper and more massive, or more severely sculpted
  Score of 5 – high vertical relief or dominant detail features
  Score of 3 – interesting erosional patterns and variety
  Score of 1 – low rolling hills or flat valley bottoms
Step 3 – Field Observation Record

## Slide 35
Vegetation
  Give primary consideration to the variety of patterns, forms, color, and texture created by plant life
  Score of 5 – variety of types and interesting patterns
  Score of 3 – some variety but only one or two types
  Score of 1 – little or no variety or contrast
Step 3 – Field Observation Record

## Slide 36
Water
  Water adds movement and serenity to a scene, the degree to which water dominates the scene affects the rating
  Score of 5 – clear, clean, still or cascading and dominant
  Score of 3 – flowing or still but not dominant
  Score of 1 – absent or present but not noticeable
Step 3 – Field Observation Record

## Slide 37
Color
  Consider the overall color in the landscape, especially focusing on the variety of colors
  Score of 5 – rich color combinations, variety and contrast
  Score of 3 – some variety but not dominant in the landscape
  Score of 1 – subtle color variations, but generally mute tones
Step 3 – Field Observation Record

## Slide 38
Influence of Adjacent Scenery
  The degree to which scenery outside the unit being rated enhances the overall impression of scenery within rating unit
  Score of 5 – greatly enhances visual quality
  Score of 3 – moderately enhances visual quality
  Score of 1 – has little or no influence
Step 3 – Field Observation Record

## Slide 39
Scarcity
  Provides an opportunity to give added importance to scenic features that may be unique within physiographic region
  Score of *5+ – one of a kind, memorable, or rare
  Score of 3 – distinctive, but not unique to region
  Score of 1 – fairly common in region
Step 3 – Field Observation Record

## Slide 40
Cultural Modifications
  Provides an opportunity to give added importance to scenic features that may be unique within physiographic region
  Score of 2 – add favorably to visual variety
  Score of 0 – add little or no variety and not discordant
  Score of -4 – add variety but very discordant
Step 3 – Field Observation Record

## Slide 41
Images from IOPs are recorded
with GPS data
Step 4 – Photo Record (IOPs)
IOP 001
IOP 002
IOP 003
IOP 004

## Slide 42
Scoring - Example
Note: Reassess and
adjust if final score
falls between
threshold of A & B
(18.5) or B & G (11.5)
Step 5 – Evaluate, Score, & Categorize
X
Rich color spectrum with
high variety of color
Score of 2. Low/Moderate
Adjacent Scenery

## Slide 43
Step 5 – Evaluate, Score, & Categorize
X
Rich color spectrum with
high variety of color
Score of 2. Low/Moderate
Adjacent Scenery
Boise

## Slide 44
Step 5 – Evaluate, Score, & Categorize
(Draft document)

## Slide 45
Step 5 – Evaluate, Score, & Categorize

## Slide 46
Example Imagery
Example of Class C Scenery

## Slide 47
Example Imagery
Example of Class B Scenery

## Slide 48
Example Imagery
Example of Class A Scenery
Example of Class A Scenery

## Slide 49
Sensitivity Level Analysis

## Slide 50
Sensitivity levels are defined as…
    (from M-8400r)
  Measure (H,M,L) of public concern for the maintenance of scenic quality
SL ratings are based on…
  Data regarding who will likely have concern about visual change and the strength of that concern
  The inventory of sensitivity indicates the public’s willingness to accept visual change by location
What is Visual Sensitivity?

## Slide 51
FLPMA recognizes scenic values and their qualitative value to the public
  (Section 102(a)(8) & 103 (c))
BLM responds to FLPMA by including visual sensitivity as an inventory “factor”—an element of scenic value
Scenic values are a quality of the human environment and subject to NEPA
Visual sensitivity determinations are pertinent for land use planning, environmental impact analysis, and for project implementation & design
Why BLM Considers Visual Sensitivity

## Slide 52
Public lands are assigned one of three possible sensitivity ratings
Sensitivity Level Analysis
  High Level of Sensitivity
    Indicates publics who generally hold a high CONCERN for retaining existing landscape character, a high INTEREST in potential visual landscape change, and a low RESILIENCE to change
  Medium Level of Sensitivity
    Indicates publics who hold a moderate CONCERN for retaining existing landscape character, a moderate INTEREST in potential visual landscape change, and a moderate RESILIENCE to change
  Low Level of Sensitivity
    Indicates publics who hold a low CONCERN for retaining existing landscape character; an accompanying low INTEREST in potential visual landscape change, and a high RESILIENCE to change

## Slide 53
High Sensitivity Examples
  National monuments
  Wilderness/WSAs/outstanding natural areas
  Scenic byways and backways
  Major transportation corridors
  Backdrops to communities
  Historic trail corridors
  Special management areas where setting is important
Low Sensitivity Examples
  OHV open areas
  Mineral or oil and gas development
    L
Sensitivity Level Analysis

## Slide 54
Sensitivity Analysis Process
1) Information Gathering Effort
4) Evaluate, Score, & Categorize SLRUs
3) Delineate Final Sensitivity Level Rating Units (SLRU)
5) Enter Data into VRI Geodatabase
2) Process and Geo-reference Accounts of Sensitivity
Visual Resource Inventory
Sensitivity Level Analysis
Public Land Visibility
Scenic Values Held by People expressed as a concern/attitude toward visual change
Delineation of Distance Zones
Land Features & Characteristics
Scenic Quality Evaluation

## Slide 55
A combination of internal and external data sources are used to inventory visual sensitivity
  Input from BLM staff is key
    Experience working with stakeholders
    Knowledge about areas that are visually sensitive to the public
    and the reason these areas are visually sensitive to the public
  Otherwise, assumptions are made that may not adequately reflect visual sensitivity within a planning area
Step 1 – Information Gathering

## Slide 56
Factors to consider:
  Types of users
  Amount of use
  Public Interest
  Adjacent land uses
  Special areas
    L
Step 1 – Information Gathering
Tehachapi Pass, Mojave, CA
Colliding Rivers, Roseburg, OR
Cripple Creek Scenic Byway Overlook
Undisturbed Float Fishing River Banks

## Slide 57
Types of users
  Sensitivity level varies by use
    Example: recreational users versus workers who pass through an area on a regular basis
    L
Step 1 – Information Gathering

## Slide 58
Amount of use
  Areas seen by large numbers of people are often more sensitive
  Protection of visual values becomes more important as the number of viewers increases
    L
Step 1 – Information Gathering

## Slide 59
Public interest
  Visual quality may be of concern
  to local, state, or national groups
  Indicators of this concern are
  usually expressed in public meetings,
  letters, newspaper or magazine
  articles, newsletters, land-use plans,
  etc.
  Public controversy created in
  response to proposed activities that
  would change the landscape character
  should also be considered
Step 1 – Information Gathering

## Slide 60
Adjacent land uses
  Interrelationships with adjacent land uses can affect visual sensitivity of an area
  For example, an area within the viewshed of a residential area may be very sensitive, whereas an area surrounded by commercially developed lands may not be visually sensitive
    L
Step 1 – Information Gathering

## Slide 61
Special Areas
  Management objectives for special areas frequently require special consideration of visual sensitivity
  Special areas include: natural areas, wilderness areas or WSA’s, wild and scenic rivers, scenic areas, scenic roads or trails, and ACECs
  These areas may not be scenic, but one of the management objectives may be to preserve the natural landscape setting
Step 1 – Information Gathering

## Slide 62
Using GIS data
  Buffer transportation or river corridors using viewshed analyses
  Use existing polygon resource data to identify other sensitive areas
Other Factors
  Consider any other information such as research or studies that include indicators of visual sensitivity
    L
Step 1 – Information Gathering

## Slide 63
Documentation
  Sufficiently documenting the sensitivity data is critical to longevity and defensibility of the inventory
  Information can be captured in table form, map form, or other means necessary to sufficiently document the information
Step 2 – Capture and Process Data

## Slide 64
The planning area is subdivided into sensitivity level rating units
  Boundaries will depend on the factor that is driving the sensitivity consideration
  Based on social characteristics and/or physical characteristics
  Can sometimes coincide with Scenic Quality Rating Units, but there does not need to be a direct correlation
  Distance zone may also play an important role
  GIS can be used exclusively
    L
Step 3 – SLRU Delineation

## Slide 65
Step 3 – SLRU Delineation
Boise
Boise

## Slide 66
Step 4 – Evaluate & Score

## Slide 67
Step 3 – SLRU Delineation
Boise

## Slide 68
Explanation and Justification is VITAL!
  This may be reviewed by
  new BLM staff, project
  proponents, etc.
  many years later
Remember……..
If you didn’t document it,
it didn’t happen!
Step 4 – Evaluate & Score

## Slide 69
Distance Zones

## Slide 70
Distance Zone Definitions
H 8410 defines distance zones as follows:
  Foreground/Middle-ground
    0 – 5 miles
    management activities can be viewed in detail
  Background
    5 – 15 miles
    Large vegetation is visible, becoming patterns of light and dark
  Seldom Seen
    >15 miles or blocked view

## Slide 71
1) Select viewing platforms
4) Evaluate, apply H-8410 DZ definitions and classify distance zones.
3) Run a computer-aided viewshed analysis using GIS
5) Enter Data into VRI Geodatabase
2) Document selection details
Visual Resource Inventory
Sensitivity Level Analysis
Public land visibility
Scenic values held by people expressed as a concern/attitude toward visual change
Delineation of Distance Zones
Land features & characteristics
Scenic Quality Evaluation
Distance Zone Process

## Slide 72
Step 1 - Select Viewing Platforms
Viewing platforms are popular ‘travel routes’ or ‘observation points’ where the general public are commonly present

## Slide 73
Step 1 - Select Viewing Platforms
Viewing platforms are popular ‘travel routes’ or ‘observation points’ where the general public are commonly present

## Slide 74
Step 1 - Select Viewing Platforms
Common practice is to select viewing platforms with consideration of public access, frequency and purpose
Consider travel routes and observation points such as
  residential developments/ population centers (city/towns),
  widely & well used roads,
  visitor centers,
  campgrounds,
  high-use trails,
  widely & well used roads,
  popular water bodies & floatable river segments,
  viewpoints/overlooks, and
  scenic railways

## Slide 75
Step 2 – Document Selection Details
Field Office
Boundary
Document info:
  Info can be gathered via text then transferred to GIS
  Data is then represented on hill-shade map with other pertinent information

## Slide 76
Step 3 – Viewshed Analysis
Current practice is to use a GIS viewshed analysis
Rather than to determine in the field by actually traveling along each route and observing the area that can be viewed
Input needed for GIS Visibility Analysis:
  Data describing what will limit visibility
    Topography/Elevation Model
    Vegetation (forest stand heights)
    Data describing the viewer location & viewers height

## Slide 77
Step 4 – Evaluate and Classify
Create 5-mile foreground/ middleground offsets from platforms
  H 8410-1, IIV. A(1)

## Slide 78
Step 4 – Evaluate and Classify
Create 15-mile background offsets from platforms
  H 8410-1, IIV. A(2)

## Slide 79
Step 4 – Evaluate and Classify
Colors assigned to Foreground/
Middleground and Background
Field Office
Boundary
Background
Foreground
Seldom
Seen

## Slide 80
Step 4 – Viewshed Analysis
Run 15-mile GIS based viewshed analysis from determined platforms to identify visible areas
  (shown in magenta)

## Slide 81
Step 4 – Evaluate and Classify
Create polygons for ‘unseen’ areas (Blue)
These polygons become the Seldom Seen distance zone
  H 8410-1, IIV. A(3)

## Slide 82
Step 4 – Evaluate and Classify
Filtering criteria may be needed if everything comes back as Foreground/Middle ground
  Review rationale for selecting viewing platforms and document any further criteria applied to change the selection
For Example:
  Highest # of people viewing for the longest time
  High public interest
  High Scenic Sensitivity (Areas of Special Designation)

## Slide 83
Distance Zone Application (Example)

## Slide 84
Distance Zone Application (Example)

## Slide 85
Distance Zone Application (Example)

## Slide 86
Distance Zone Application (Example)

## Slide 87
Step 4 – Evaluate and Classify
Boise

## Slide 88
Step 4 – Evaluate and Classify
Boise

## Slide 89
Viewshed Analysis
Considering the Distance Zone Information:
  Results of this analysis provide insight at the planning-level about where:
    lands are most exposed to the viewing public
    the BLM’s management actions will be on display & open to the public’s general criticism or praise – more so than other places
    to explore alternative siting options, if appropriate, when an activity is proposed

## Slide 90
INVENTORY
  is the effort to identify and document information about existing scenic values
EVALUATION
  is also done as part of the inventory process
VRI Recap
VRI Classification
Visual Resource Inventory
Scenic Quality Evaluation
  Land Features & Characteristics
      What does it look like?
Sensitivity Level Analysis
  Scenic Values Held by People expressed as a concern/attitude toward visual change
    Importance to the public
Delineation of Distance Zones
  Public Land Visibility
    Where do people view the landscape and how?

## Slide 91
How are VRI classes determined?
VRI Class Determination Table

## Slide 92
VRI Classes
B
Low
FG/MG
Scenic Quality
Sensitivity
Distance Zone
High

## Slide 93
VRI Classes
Boise

## Slide 94
Value of Inventories
  Methodology is the same across all BLM field offices
  Intent, that the VRI is a living document that can be updated
  One inventory serves the planning area
  Serves as a basis for NEPA analysis for comparing the existing condition to a proposed condition in order to identify how the change would affect scenic quality
  Allows analysis to determine scarcity levels of a particular visual value
  Provides basis to consider visual values in the land use planning process
    L
Visual Resource Inventory
Closing Remarks

## Slide 95
Future considerations
  Within the inventory units (SQRU, etc.) has anything changed?
  If so, capture the changes
    Keep VRI current
    Bring forward into NEPA analysis for proposed projects
Remember……..
If you didn’t document it, it didn’t happen!
    L
Visual Resource Inventory
Closing Remarks