## Slide 2
Contrast Rating

## Slide 3
Contrast Rating
Unit Objective
Determine the elements of a project that are inconsistent with VRM objectives and recommend measures to improve the visual quality of the project
The VRM System is about minimizing visual contrast
The Contrast Rating process
First, determines whether a proposal conforms to the current Land Use Plan, and
Second, supports the subsequent impact analysis process

## Slide 4
Contrast Rating
Process
A systematic process used to analyze potential visual impacts of proposed projects and activities
  BLM Handbook 8431-1
The amount of contrast is measured by separating the landscape into major features
  Landform/water, vegetation, and structures
  Use “language of landscapes” when describing
Then predicting the magnitude of contrast in each of the basic elements
  Form, line, color, and texture

## Slide 5
Contrast Rating
Process
Quickly reveals elements and features that cause the greatest visual impact
Intended to assist BLM personnel not formally trained in the design arts to apply basic principles of planning and design to prevent or minimize visual impacts
Every attempt should be made to reduce visual impacts even if a project meets VRM objectives for the area

## Slide 6
The contrast rating should be completed in the field from the selected KOP(s) and should be completed by an interdisciplinary team
Do not fill out forms as a “desk exercise,” it is important to get out on the ground to see the context of the proposed project and its location
The contrast rating should be completed during the time of year and time of day when most people will be viewing the area of development
Contrast Rating
Tips

## Slide 7
Work with project proponent early in the project planning process, this will help prevent surprises later!
  1 – Obtain a complete project description
  2 – Identify VRM objectives from land use plan
  3 – Select Key Observation Points (KOPs)
  4 – Prepare visual simulations (optional)
  5 – Complete contrast rating
Contrast Rating
Steps

## Slide 8
Obtain a complete project description
  Emphasize early contact with project proponent
  Coach proponent on project design
  Project proposal must be comprehensive (who, what, when, where, and why)
  Details are important
Contrast Rating
Step 1 – Project Description

## Slide 9
Identify VRM objectives from the land use plan
  Familiarize yourself with your land use plan
  Identify VRM objective
    What is the existing management class for the project location and why?
  Involve interdisciplinary team
  Understand other resource issues
Contrast Rating
Step 2 – VRM Class Objectives

## Slide 10
Contrast Rating
Step 2 – VRM Class Objectives
OBJECTIVE | Class I | Class II | Class III | Class IV
Management | preserve, manage for natural ecological changes | retain | partially retain | major modification
Change Allowed | very low | low | moderate | high
Visibility | activities should not be visible and must not attract attention | activities may be visible, but must not attract attention | activities may attract attention but should not dominate the view | activities may attract attention, may dominate the view, but are still mitigated

## Slide 11
Select Key Observation Points (KOPs)
  What is a KOP?
    A critical viewpoint or place from
    which we analyze the visual impact
    of a proposed project
Types of KOPs
  KOPs should be places from which a proposed project is seen by large numbers of viewers or critical viewers
  Where view of proposed project is most revealing
  Single Points – trailheads, campgrounds, scenic overlooks, parking lots, subdivisions, and towns
  Linear – roads, trails, and rivers
Contrast Rating
Step 3 - KOPs

## Slide 12
Factors in KOP selection
  Remember the Environmental Factors!
    Angle of observation
    Number of viewers
    Length of time the project is in view
    Relative project size
    Season of use
    Light Conditions
How many KOPs are needed?
  Linear projects should have more than one
  Dependent on the size of the project, land use plan direction, locations from where it can be seen
Contrast Rating
Step 3 - KOPs

## Slide 13
When are KOPs selected?
  Early in the project planning
  process
Who selects them?
  Interdisciplinary team
  Input from proponent
  Coordination with other agencies
    Examples - NPS and USFS
Accuracy is important!
  Location can sway results
Contrast Rating
Step 3 - KOPs

## Slide 14
Prepare visual simulations (optional)
  Larger, complex projects may benefit from visual simulations
  Provides visual representation of a project before and after
    Highlights impacts and potential mitigation measures
    Good way to illustrate impacts in NEPA analysis
    Seeing an image of a project is much more powerful than trying to imagine it
    Helps eliminate bias
    Allows all team members to see the project the same
    Helps the proponent, public, and the BLM
Contrast Rating
Step 4 – Visual Simulation(s)

## Slide 15
Contrast Rating
Step 4 – Visual Simulation Example
Before – Existing Conditions
After - Simulation
Mitigated Simulation

## Slide 16
Complete Contrast Rating
  Visual Contrast Rating Worksheet – BLM Form 8400-4
  See BLM Handbook H-8431-1
  Validates Land Use Plan Conformance
  Provides documentation for NEPA
  Provides a record for future action
  Helps defend against appeals
Contrast Rating
Step 5 – Contrast Rating

## Slide 17
Contrast Rating
Step 5 – Contrast Rating Worksheet
Use separate sheets for multiple KOPs

## Slide 18
Contrast Rating
Worksheet
Section A

## Slide 19
Contrast Rating
Worksheet
Section B

## Slide 20
Contrast Rating
Worksheet
Section C

## Slide 21
Contrast Rating
Worksheet
Section D

## Slide 22
Contrast Rating
Step 5 – Contrast Rating Worksheet
Section A
  Locates the project and identifies the VRM class
  A simple illustration or map identifies the project location and KOP

## Slide 23
Contrast Rating
Step 5 – Contrast Rating Worksheet
Section B
  Where the existing characteristic landscape of the project area is described (use “language of landscapes”)
  Focus on the area being affected by the project

## Slide 24
Section C
  Determine the type of feature a project fits under
  A project might fit under more than one
Contrast Rating
Step 5 – Contrast Rating Worksheet
Landform/Water Features | Vegetative Features | Structural Features
Roads | Timber Harvests | Transmission Lines
Mining | Grazing Systems | Generation Plants
Gravel Pits | Habitat Treatments | Oil & Gas Development
Water Impoundments | Fuel Treatments | Recreation Facilities
 |  | Water Tanks
 |  | Microwave Stations
 |  | Buildings

## Slide 25
Contrast Rating
Step 5 – Contrast Rating Worksheet
Section C
  Where the proposed activity’s effects on the characteristic landscape are described

## Slide 26
Section D
  Projects may be rated on either a short-term or long-term basis
    Short-term is through the first 5 years
    Long-term is through the life of the project
  If the project has different short-term and long-term effects, two contrast ratings should be completed
Contrast Rating
Step 5 – Contrast Rating Worksheet
X

## Slide 27
Section D
  Organized into features (land/water, vegetation, and Structures) and elements (form, line, color, and texture)
Contrast Rating
Step 5 – Contrast Rating Worksheet

## Slide 28
Section D
Contrast Rating
Step 5 – Contrast Rating Worksheet
IV
III
II
I
IV
III
II
I
IV
III
II
I

## Slide 29
Section D
  Example – if a project demands attention and is dominate, it creates a strong degree of contrast. It would conform to the class IV objective ONLY and would not conform to class I, II, or III objectives
Contrast Rating
Step 5 – Contrast Rating Worksheet
IV
III
II
I
IV
III
II
I
IV
III
II
I
x
x
x
x
x
x
x
x
x
x
x
x

## Slide 30
Section D
  Example – if a project can be seen but does not attract attention, it creates a weak degree of contrast. It would meet Class II, III, and IV objectives
  It would not meet the Class I objective
Contrast Rating
Step 5 – Contrast Rating Worksheet
IV
III
II
I
IV
III
II
I
IV
III
II
I
x
x
x
x
x
x
x
x
x
x
x
x

## Slide 31
Section D
  In this example, a project is proposed in VRM Class III
  The project would meet VRM Class III for all features and elements - except structures where there is strong contrast in line, color, and texture
Contrast Rating
Step 5 – Contrast Rating Worksheet
IV
III
II
I
IV
III
II
I
IV
III
II
I
X

## Slide 32
Section D
  This tells you where to focus mitigation efforts in order to reduce the degree of impact, and thus meet the VRM objective
  Additional mitigation measures would be recommended for the structure’s elements of line, color, and texture
Contrast Rating
Step 5 – Contrast Rating Worksheet
IV
III
II
I
IV
III
II
I
IV
III
II
I
X

## Slide 33
Contrast Rating
Step 5 – Contrast Rating Worksheet
Section D (Continued)
  Where you can provide further explanation of why a project does or does not meet VRM objectives
  As in this example, changes to land and vegetation would cause a moderate degree of contrast to the element line
  The element line is a focus for mitigation efforts for this project

## Slide 34
Contrast Rating
Step 5 – Contrast Rating Worksheet
Section D (Continued)
  Where you can provide recommended mitigation measures

## Slide 35
  Conformance with VRM Objectives
    Does project meet VRM Objectives?
      NO, what to do?
      Redesign project to meet VRM Objectives
      Internally initiated – Drop project
      Externally initiated – Deny application for project
      Amend RMP only as a last resort
        Address reasons for the current VRM Class designation
        Assess offsite mitigation
Contrast Rating
Step 5 – Contrast Rating Worksheet

## Slide 36
Contrast Rating
Process (Continued)
Document!
  Take pictures
  Complete the form
  Write short narratives
  Prepare visual simulations (optional)
  Do whatever you need to do to describe your thought process and final recommendations
  Documentation is the only way you or your manager will accurately remember what took place during your analysis
  And if challenged, no documentation = didn’t happen

## Slide 37
Contrast Rating
Process (Continued)
Input information into NEPA document
  Enter your findings, along with necessary documentation
  Write any necessary stipulations
    Be sure all resource stipulations are coordinated and in agreement
Continue to work with the project proponent through all phases of the project (pre-construction, construction, and reclamation) to ensure project is completed as planned and stipulations are being followed!
Patience! It may take years before you see the outcome of all your efforts

## Slide 38
Contrast Rating
Example – New Natural Gas Well Pad
1 – Obtain a complete project description
  Proposal to drill 8 new federal wells from a new well pad with new access road on land administered by the BLM
  Well pad would have a maximum cut slope of 33.1 feet at the southwest corner and a maximum fill slope of 25.2 feet at the northwestern corner
  The road would be approximate 0.4 mile in length and 20-feet in width
  The road grade would vary from 5% to 10%
  Installation of a temporary pipeline
  Construction would involve approximately 7.9 acres of new surface disturbance, which would be reduced to approximately 2.5 acres after interim reclamation

## Slide 39
Contrast Rating
Example – New Natural Gas Well Pad
2 – Identify VRM objectives
from land use plan
  Class II
    Retain landscape character
    Change allowed: low
    Visible but should not attract
    attention
  Class III
    Partially retain landscape
    character
    Change allowed: moderate
    Can attract attention but
    should not dominate view

## Slide 40
Contrast Rating
Example – New Natural Gas Well Pad
2 – Identify VRM objectives
from land use plan
  Class IV
    Provide for management
    activities which require
    major modification to the
    character of the landscape
    Change allowed: high
    Activities may attract
    attention, may dominate the
    view, but is still mitigated

## Slide 41
Contrast Rating
Example – New Natural Gas Well Pad
3 – Select Key Observation
Points (KOPs)
  Linear features – State
  Highway 6 and County Road
  300
  3 KOPs were selected based
  on field analysis and
  from environmental factors
  (e.g. angle of view, season
  of use, duration in view)

## Slide 42
Contrast Rating
Example – New Natural Gas Well Pad
4 – Prepare visual simulations (optional)
  KOP 2
Before
During Construction
Before – Existing Conditions
Simulation - Mitigated

## Slide 43
Contrast Rating
Example – New Natural Gas Well Pad
5 – Complete contrast rating

## Slide 44
Contrast Rating
Example – New Natural Gas Well Pad
Patience........................
During Construction
Post mitigation
Notes: It can take years to see the outcome of all the effort, particularly relating to reclamation that meets BLM standards.

## Slide 45
Contrast Rating
Class Exercise # 1
Notes: It can take years to see the outcome of all the effort, particularly relating to reclamation that meets BLM standards.

## Slide 46
Contrast Rating
Class Exercise
After - Simulation
Before – Existing Condition
Notes: It can take years to see the outcome of all the effort, particularly relating to reclamation that meets BLM standards.

## Slide 47
NEPA
Notes: It can take years to see the outcome of all the effort, particularly relating to reclamation that meets BLM standards.

## Slide 48
National Environmental Policy Act
  Signed into law on January 1, 1970
  Landmark environmental policy
  Encourages environmental protection and informed decision-making
NEPA

## Slide 49
Determination of NEPA Adequacy (DNA)
  Proposed Action is adequately analyzed in existing NEPA document(s)
Categorical Exclusion (CX)
  Proposed Action predetermined to NOT have significant effect on the quality of the human environment (individually or cumulatively)
  Statutory, Departmental, or BLM categorically excluded
  Lacks extraordinary circumstances (ex. T&E, WA/WSA, wetlands, etc.)
Environmental Assessment (EA)
  Used to determine IF Proposed Action would have significant effects
Environmental Impact Statement (EIS)
  Proposed Action WOULD result in significant effects
NEPA
Types of NEPA Documents

## Slide 50
Prepared by BLM specialists:
  Internal – rec site, range improvement, fuels reduction
  External – single pad oil & gas well, communication site
Prepared by others but reviewed by BLM specialists:
  Land Use Plan revisions
  ROW for utility-scale renewable energy development
  ROW for transmission line / natural gas line
NEPA
Types of NEPA Efforts

## Slide 51
Project Proponent
Resource Management Plan
Knowledge from Resource Specialists
Visual Resource Inventory
Field Review of Project Proposal
Completed Contrast Rating Form
Input from Affected Landowners
Associated Consulting Firms
Input From the General Public
Similar Projects (including images) / Visualizations
NEPA
Sources for Visual Documentation

## Slide 52
Introduction
  Background
  Project location
  Purpose and Need
  Plan Conformance
    What is the VRM Class where project is proposed?
    Is project allowable per RMP guidance?
    Can it meet VRM objectives?
NEPA
NEPA Document - Chapter 1

## Slide 53
Scoping: Issue identification
  Internally generated (IDT Checklist)
  Externally generated (public scoping)
  What are visual concerns related to the proposed project?
  Entire resources are NOT issues
  Issues drive design features and alternative development
NEPA
NEPA Document – Chapter 1 Continued
EXAMPLE LANGUAGE:
  Will the proposed site developments create visually contrasting impacts that alter the landscape character?

## Slide 54
Scoping: Issue identification
    Example: How would constructing, operating and maintaining a 159 turbine wind energy facility alter the landscape character?
NEPA
NEPA Document – Chapter 1 Continued

## Slide 55
Interdisciplinary team checklist
NEPA
NEPA Document – Chapter 1 Continued

## Slide 56
Proposed Action & Alternatives
  Alternative development
    Develop alternatives that meet VRM objectives
    What would it take for project to conform?
    Forces early consideration of visual design solutions when preparing alternatives
    Establishes a range of design features and/or mitigation measures
    Allows for better evaluation of trade-offs and benefits
    Allows for informed decision making
NEPA
NEPA Document – Chapter 2

## Slide 57
Alternatives Content
  Complete project descriptions for each alternative
  Who, what, when, where, how, and why
  Photos of similar projects or visualizations can be very helpful
NEPA
NEPA Document – Chapter 2 Continued

## Slide 58
NEPA
NEPA Document – Chapter 2 Continued
Alternative B: BLM would develop a parking area adjacent to Dance Hall Rock Historic Site on the east side of the Hole in the Rock Road. Development would occur in a previously undisturbed area and include the following:
constructing parking for approximately 12 vehicles including two oversize ones
installing a vault toilet
constructing a 500-foot entrance road for ingress and egress to the parking area
installing interpretive panels
installing site signage
constructing a 500-foot trail from the parking area to the edge of Dance Hall Rock
Improvements would include hardening the parking area and road surface with road base. Equipment that would be used to develop this project would likely include hand tools, dump trucks, front end loaders, road graders and a tractor trailer with crane to install the vault toilet. The earliest the project would be implemented is Fall 2014. Implementation and completion of the project is estimated to be one month from when construction starts.
Design criteria to meet built environment image guidelines and other guidance would include the following:
Natural or natural-appearing materials would be used. These could include concrete, natural stone, gravels or fines, rusted or painted metal, and/or wood. No shiny, reflective materials would be used.
Natural palette colors would include grays, reds, salmons, rusts, browns, and buffs. No bright colors such as whites or yellows would be used.

## Slide 59
Affected Environment
  Describe Characteristic Landscape
    Use VRI
    Use Section B of the Contrast Rating Form(s)
NEPA
NEPA Document – Chapter 3

## Slide 60
Affected Environment
NEPA
NEPA Document – Chapter 3 Continued
  VRM Objectives

## Slide 61
Affected Environment Continued
  Describe the casual observer(s)
  Explain VRM Class Objectives
NEPA
NEPA Document - Chapter 3 Continued

## Slide 62
Environmental Effects
  Need to be quantified / qualified
  Determine conformance with VRM objectives
    A statement like: “The project would (or would not) impact visual resources is NOT sufficient.”
  The Environmental Impact is the amount of contrast the project causes to the existing landscape.
  Identify the KOP(s) and why selected.
  Explain influence of any Environmental Factors.
  Refer to Sections C and D on the Contrast Rating Form.
  Describe the nature of the impact - use terms WEAK, MODERATE, STRONG - and include language from narrative on back of Contrast Rating Form.
NEPA
NEPA Document – Chapter 4

## Slide 63
Environmental Effects
NEPA
NEPA Document – Chapter 4 Continued
SECTION C. PROPOSED ACTIVITY DESCRIPTION |  |  | 
 | 1. LAND/WATER | 2. VEGETATION | 3. STRUCTURES
FORM | Same . | Same. | Boxy forms associated with toilet and automobiles. Curving swatch of new entrance road and irregular horizontal form parking area.
LINE | Same. | Same. | Horizontal, vertical, curving band.
COLOR | Same. | Same. | Reds and salmons, grays, browns and tans, earth-tones – multi-color intermittently when autos are parked on site.
TEX- TURE | Same. | Same. | Smooth to medium.

## Slide 64
Environmental Effects
NEPA
NEPA Document – Chapter 4 Continued
Section D, continued (from back of Contrast Rating Form)
For Alternative B as viewed from KOP 2 has the development located in a depression where the landform rolls away and down from this viewing angle, thus partially screening the features associated with it. The casual observer would see the upper portions of the vault toilet, portions of the intermittently-parked vehicles and possibly some portions of the other site features. The toilet and other features would be of colors and textures to blend with the natural landscape character. The automobiles of all colors would be the most noticeable items but would be parked

## Slide 65
4 - Environmental Effects Continued
NEPA
NEPA Document – Chapter 4
BLM’s Visual Resource Management program includes a standardized system to review lands actions for resource management plan conformance. Visual contrast rating worksheets are completed to determine if a project conforms to the resource management plan. In order to evaluate the environmental consequences of the alternatives for this proposed project, three key observations points (KOPs) were established as part of completing the contrast rating analysis.
KOP #1 was along Hole in the Rock Road looking south toward the sites; KOP#2 was also along Hole in the Rock Road but looking north toward the sites; and KOP#3 was on the floor of Dance Hall Rock looking outward across the landscape. The visibility of the alternatives from these KOPs is detailed in the table below.
Comparison of Visibility by Alternative from Key Observation Points
Hole in the Rock Road closely follows the path of the Mormon San Juan Mission expedition route, is a State Scenic Backway, and provides access to many popular recreation destinations in GSENM and Glen Canyon National Recreation Area for thousands of visitors annually, hence the justification for selecting two KOPs along it from both travel directions. The third KOP, on the Dance Hall Rock amphitheater floor looking outward, was selected per feedback from public scoping from those concerned about the preservation of the views from inside the historic site outward.
 | KOP#1 | KOP#2 | KOP#3
Alt A: No Action | Not Visible | Minimally Visible | Fully Visible
Alt B: Existing Disturbance Area | Not Visible | Partially Visible | Fully Visible
Alt C: New Disturbance Area | Partially Visible | Fully Visible | Not Visible

## Slide 66
4 - Environmental Effects Continued
NEPA
NEPA Document – Chapter 4
BLM’s Visual Resource Management program includes a standardized system to review lands actions for resource management plan conformance. Visual contrast rating worksheets are completed to determine if a project conforms to the resource management plan. In order to evaluate the environmental consequences of the alternatives for this proposed project, three key observations points (KOPs) were established as part of completing the contrast rating analysis.
KOP #1 was along Hole in the Rock Road looking south toward the sites; KOP#2 was also along Hole in the Rock Road but looking north toward the sites; and KOP#3 was on the floor of Dance Hall Rock looking outward across the landscape. The visibility of the alternatives from these KOPs is detailed in the table below.
Comparison of Visibility by Alternative from Key Observation Points
Hole in the Rock Road closely follows the path of the Mormon San Juan Mission expedition route, is a State Scenic Backway, and provides access to many popular recreation destinations in GSENM and Glen Canyon National Recreation Area for thousands of visitors annually, hence the justification for selecting two KOPs along it from both travel directions. The third KOP, on the Dance Hall Rock amphitheater floor looking outward, was selected per feedback from public scoping from those concerned about the preservation of the views from inside the historic site outward.
 | KOP#1 | KOP#2 | KOP#3
Alt A: No Action | Not Visible | Minimally Visible | Fully Visible
Alt B: Existing Disturbance Area | Not Visible | Partially Visible | Fully Visible
Alt C: New Disturbance Area | Partially Visible | Fully Visible | Not Visible

## Slide 67
NEPA
NEPA Document – Chapter 4
The potential project locations are within close proximity to Hole in the Rock Road, contributing to their visibility. Visitors travel in this area year round though peak visitation is in the spring and fall months. For those travelling the road in either direction, the length of time the sites would be in view is less than a minute, but for those spending time at the site, Alternative B would be visible as long as their visit lasts. The massiveness of Dance Hall Rock would dwarf the site improvements in terms of scale.
Alternative B
During construction, temporary visual impacts would result from the visibility of construction equipment and site work. Post-construction, the contrast created by the site improvements would be negligible in regards to the changes in vegetation. Weak landform contrast would be created in line and form by the delineation of the parking area and the structures (i.e. toilet, signs, etc.) due to adding blocky, randomly-spaced elements with vertical, horizontal, and diagonal lines into the landscape. Additionally, the vehicles that park to use the area would be visible and would create minor visual contrast, though they would be transitory.
In order to minimize the visibility of the site development for those travelling along Hole in the Rock Road, it would be sited in a depression surrounded by landforms. The toilet and other fixtures would be constructed of materials that blend with the natural environment minimizing the color and textural contrast they would create.

## Slide 68
Environmental Effects
  Cumulative Effects
    Impact on the environment which results from incremental effect of past, present, and reasonably foreseeable future actions (no matter who undertakes them)
  Determine Cumulative Impact Area
  Assess quantitatively if possible
NEPA
NEPA Document – Chapter 4 Continued

## Slide 69
Environmental Effects Continued
NEPA
NEPA Document – Chapter 4 Continued
Cumulative Impact Area (CIA)
Visual Resources - The cumulative impact area of analysis for Visual Resources is the viewshed along Hole in the Rock Road.
Cumulative Impact Analysis
The cumulative impacts to visual resources from past, present, and reasonably foreseeable actions include establishment of livestock grazing management facilities (corrals, fences, water developments, storage buildings, etc.), recreational facilities (trailheads, day use areas, etc.), general recreational use, and road construction and maintenance activities. The action alternatives would not contribute to a measureable increase in impacts to visual resources as they would be constructed to blend with the landscape, be screened from view to the extent practicable, and the Dance Hall Rock location is already an attraction visited by the general public on a regular basis. Additionally, the Hole in the Rock Road runs for more than 60 miles from north to south through a viewshed that encompasses a landscape of 100,000s of acres. This development would be visible only when in near proximity to the site and is small in scale within this grand scale landscape.

## Slide 70
Environmental Effects
  Does project meet VRM Objectives?
      YES, if:
NEPA
NEPA Document – Chapter 4 Continued
  None = Class I
  Weak = Class II
  Moderate = Class III
  Strong = Class IV

## Slide 71
Environmental Effects
NEPA
NEPA Document – Chapter 4 Continued
Alternative B
By constructing the project according to the outlined design criteria and implementation measures, the minor changes to the existing character of the landscape would be appropriate to meet the visual resource management objectives of the area.

## Slide 72
Environmental Effects
NEPA
NEPA Document – Chapter 4 Continued
Alternative B
By constructing the project according to the outlined design criteria and implementation measures, the minor changes to the existing character of the landscape would be appropriate to meet the visual resource management objectives of the area.

## Slide 73
Environmental Effects
  Does project meet VRM Objectives?
      NO, what to do?
      Redesign project to meet VRM Objectives
      Internal – Drop project
      External - Deny application for project
      Amend RMP
    List of preparers
    Agencies consulted
NEPA
NEPA Document – Chapter 4 Continued

## Slide 74
References
  Bureau of Land Management (BLM). 1986. BLM Manual Handbook 8410-1-Visual Resource Inventory
  Bureau of Land Management (BLM). 1986. BLM Manual Handbook 8431-1-Visual Resource Contrast Rating
NEPA
NEPA Document – Chapter 5

## Slide 75
  Are we done once NEPA is completed?
  Is it time to go fishing?
NEPA

## Slide 76
NEPA
  NO?!!
  Sooooo, What’s next?

## Slide 77
NEPA
Build it and check to see if you did okay………….
AKA - Monitoring